# Access Road Construction – Nyngan Solar Plant

Knowledge type: Construction

Knowledge category: Technical

Technology: Solar photovoltaic

## Key learning

Thorough preparation and execution of the access road works is important to ensure timely delivery of the project. Any delays in delivery (i.e. weather) will impact the project delivery schedule as the majority of site works occur after the completion of the access road.

## Implications for future projects

There will be limited duplication in this area for the Broken Hill project, with site dynamics different from a topographic and geotechnical perspective. The Nyngan project experience did lead to a heightened sense of urgency for access road construction as well as awareness about delay risk related to weather and CEMP.

## Knowledge gap

No knowledge gaps were identified for the access road construction. The capability of local contractors is consistent with global standards in this area.

## Background

### Process undertaken

Access road was constructed between the Barrier Highway and the Nyngan Solar Plant. The original plan was to build the road at the existing ground level, but heavy rain and flat ground made it necessary to increase the elevation of the road to facilitate site access in the event of heavy rains.

### Supporting information

Photo: Original site access road after heavy rain

Photo: Original site access road before heavy rain