# Local supply chain responsiveness, limitations and areas for improvement – Nyngan Solar Plant

Knowledge type: Construction

Knowledge category: Technical

Technology: Solar photovoltaic

## Key learning

- Local supply chain is non-existent for standard products in foreign markets (e.g.  I-Beam posts used in the USA could not be sourced in Australia)

- For imported products, foreign suppliers are often unfamiliar with Australia Standards and sometimes with export requirements

- Imported products increase lead time and shipping costs

- Local suppliers unfamiliar with the technical requirements of Utility scale Solar Farms

- Local suppliers have a higher expectation of specification level than US suppliers i.e. the Australian expectation is a fully engineered design specifications not a performance specification. This results in more time and resources being dedicated early on in the project.

## Implications for future projects

- Work directly with Original Equipment Manufacturers (OEM’s) for critical equipment i.e. Photovoltaic Combining Switchgear (PVCS)

- Develop clearly defined and documented Scope of Works (SOW) and Divisions of Responsibilities (DOR)

## Knowledge gap

The primary knowledge gap for supply chain in the Australian solar industry is the historic absence of a utility scale solar supply chain in Australia. This can be best summarised as follows:

- Absence of local manufacturing of key components – PV modules, inverters.

- Absence of local manufacturing of enabling components – mounting structures, inverter/transformer integration, combined boxes, cables.

First Solar has worked primarily on localising the majority of the enabling works, much of which is detailed in the attached brochure.

## Background

### Objectives or project requirements

See industry capability brochure attached.

- First Solar has organised 2-way knowledge sharing sessions  between US suppliers and local suppliers i.e. IXL/OMCO, Ampcontrol/Fibrebond

- Continue to work with local suppliers to drive process efficiencies and cost reduction opportunities

### Supporting information

Photo: Table assembly

Photo: Table Assembly

Photo: Shipment of tables

Photo: Adelaide to Nyngan route for module/table shipment